## Slide 1: VLAN – not a firewall.
Paul Horgan

## Slide 2: So what is a VLAN
A VLAN is a virtual LAN
You can segment your LAN in a cost effective way
You can filter by MAC address, IP address or even port number
The following example uses a router, but newer level 3 switches have the functionality built in
A VLAN is a cost effective way to segment your network
Easier to manage (if the documentation is good)
VLANS are a product of the dark times, when switches were hubs, snickers was marathon and music was good.

## Slide 3: VLAN vs Firewall
A VLAN is NOT a firewall
The security a VLAN gives is a byproduct, not the focus of the config
A VLAN does NOT replace a firewall
They operate at layer 2 (the Ethernet layer) and don't understand the “state” of the messages flowing through them

## Slide 4: VLAN Scenario
Scenario :
A restaurant has 3 distinct networks :
Point of Sale
Backoffice
Guest Wi-Fi
Point of Sale takes orders from the bar etc.
Backoffice is where the accounts package, maybe mail server and where backups are kept
Guest Wi-Fi is internet access for guests

## Slide 5: Enterprise scenario
Office has :
Servers
Workstations
Printers
IP telephony
Reasonably you would VLAN printers and IP telephony apart from all other endpoints at a minimum

## Slide 6: Inter VLAN routing
Using ACL (Access Control Lists) you can control which VLANs can see each other.
You can route by source MAC address or VLAN
Example :
Only route traffic from VLAN 1 to VLAN 2 if the traffic is on port 80
Deny traffic from VLAN 1 to VLAN 3

## Slide 7: Demo Time
Build out a network such that :
VLAN 10 = 192.168.10.XX
VLAN 20 = 192.168.20.XX
VLAN 30 = 192.168.30.XX
VLAN 1 should see VLAN 2
VLAN 2 should see VLAN 1
VLAN 3 has no access to anything
The default switch ports should have no access